## Slide 1: Pac-Lite Hardware Benchmark
Devlin Paddock | 06/12/19
Light is OSRAM
Automotive

## Slide 2: Why do we need Pac-Lite
Camstar
    A Manufacturing Execution System.
    Communicates primarily in XML UDP packets
    Receives information directly from Pac
Pac
    A Process Automation Control software
    A Machine abstraction layer that allows communication between machine controls and Camstar
    Doesn’t mesh well with legacy machines
    $ 1000 license per machine
Pac-Light
    Black box to allow legacy machines to communicate with Camstar in the absence of an MDE
    Provides basic functionality for Camstar modules without the time and expense of a full blown MDE system but lacks the features of a full MDE system
Camstar
Pac Lite
Legacy Machines
Pac
Machines
TCP XML
MDE
Packetized data
UDP Packet
Digital IO
Engineering Database
ActiveMQ

## Slide 3: Pac-Lite Project Requirements
Report Machine Output
    Up/Down status
    Good/Bad part output
    Machine indexes
    Empty head
    What product is being produced
    Enable power on
    10 Input to pac-lite
Display Machine Status
    Status stack light
    Easy to use HMI
    4 outputs from pac-lite
HMI
    Product selection- NAED
    Defined DT button
    Self managed NAED list
    Display diagnostics.
Sample UI on a Siemens HMI
New NAED
Enter
Sort
Camstar
Pac Lite
Legacy Machines
Pac
Machines
Scope of the project in orange
MDE
MQTT Packets
Digital IO
Cancel
Notes: Reduce slightly.

## Slide 4: Proposed Pac Light Architectures
One CPU per machine solution
    Provide a local HMI for user input, information and diagnostics display.
    Easy for E-Techs to troubleshoot
    Reliably record output of a single machine and report it to Camstar
One CPU per three machine solution
    Integration with up to three target machines
    Provide up to four remote HMIs for user input, information and diagnostics display.
    Reliably record output of up to three machines and report it to Camstar as separate machines.
One CPU per line solution
    One remote IO bundle per machine.
    Provides one display at beginning or end of line
    Reliably record output of up to 32 machines and report it to Camstar as separate machines.
Machine
Pac Lite
Pac Lite
HMI
HMI
HMI
HMI
Machine
Machine
Machine
Pac Lite
Machine
Machine
Machine
HMI
HMI
Notes: //Add original project def slide to backup slides. Add backup slides section after final slide.
//look into possibility of 1 HMI instead of 4. restriction was on HMI’s I believe that it was limited to 128 IO expansion at 8 per remote IO max.
//Check out support for communicating Between two plc’s in the 1200 series to allow switching the NAED at one location instead of two.
Replace diagrams on right with images of siemens pc’s
Shift slide 10-11 in as well

## Slide 5: Architecture Hardware
Scada
    Single machine architecture
    Limited by IO and HMI
1212C
    Single, Three machine, or line based architecture.
    Limited by number of HMI’s.
    Siemens remote IO for multiple machines.
1510SP
    Four Machines, or line based architecture
    Limited by number of HMI’s
    No integrated IO, requires remote IO or expansion.
Machine
Pac Lite
Pac Lite
HMI
HMI
HMI
HMI
Machine
Machine
Machine
Pac Lite
Machine
Machine
Machine
HMI
HMI

## Slide 6: SCADA Box ,One Machine solution
Operating System:
    An IPC Linux operating system.
    Higher level language allows for more communication flexibility
Hardware
    Beagle Bone Black base
      4 GB internal storage
      Relevant IO
        USB, Micro HDMI,8 digital in, 8 digital out and 8 analog in.
HMI
    Freeboard Remote HMI for administration
    Node Red Local HMI for management of the machine and NAED selection.
    Outputs over HDMI allowing for much more freedom in
    display choices.
Free Board
Local HMI
C/C++
Node Red
Gamma
Middleware
IO
Also Supports High chart and Xibase Integration

## Slide 7: Siemens Products -Generic
Hardware
    Limited number of connections that has to be split between Web, IO, HMI, Etc.
    Expandable by IO and communication Modules.
      Communication: Serial, Profibus, Profinet, Etc.
      IO: Timers, PWM output, analog, Relay, Etc.
Profinet Connection
“Smart” HMI
CPU
Memory
IO
Other Controllers
Remote IO
Software
    Developed in Step7 or Tia Portal.
    Scan Based OS
    Lower level control.
    Requires HMI Displays capable of rendering themselves.
Notes: Go into hardware more indepth glossed over before

## Slide 8: CPU solutions
1212C
    8 inputs and 6 outputs integrated
    Supports 3 HMIs
    Remote IO Via Profinet
    Lacks STL, and Graph support
    Lower cost than 1500 series. Larger footprint
    Slower operation speeds.
1510SP
    No integrated IO
    Supports 4 HMIs
    Remote IO via Profinet
    Supports STL, and Graph
    More expensive than 1200 series
    Fast operation speeds

## Slide 9: SCADA box Benefits
Higher Level Control:
    Easy deployment
      Administrative Free Board
      Local Node-Red HMI
    Different communication types
      MQTT,HTTPS,UDP,TCP Etc.
    Remote machine control
      Can poll servers for BOM data or machine lock signals
Useful for later Projects
    Adds a lot of resident IO
      2 Serial, 4 thermal interfaces, 8 analog Inputs, IDRA receiver
    Can be reused for other projects
      Could addon Environment monitoring
Misc.
    Web based management
    35% cheaper than 1212C and 22% cheaper than 1510sp across 6 machines

## Slide 10: Siemens Solution Benefits
Better Maintainability:
    Local Factors
      Local Experience
      Replacement Parts
    Common Development Environment
      Better Forums
IO Expansion
    More IO available for more in depth error reporting
    Communication Modules
      Ability to add Serial, Profinet, Ethernet, Profibus, Etc.
Misc.
    Easy to deploy
    Easy to troubleshoot
    Durability tested to -20C, and 15g shock, IP20 protection rating

## Slide 11: Cost Breakdown
 | 1212C Single | Scada Single | 1510 Multi | 1510 Line
Cost for 1 machine | $830 | $536 | $1,730 | $2,077
Cost for 4 Machines | $3,320 | $2,144 | $3,995 | $3,301
Cost for Straight Base | $4,979 | $3,216 | $6,480 | $4,117
Chart: 
1212C | 829.9 | 1659.8 | 2489.7 | 3319.6 | 4149.5 | 4979.4 | 5809.3 | 6639.2 | 7469.1 | 8299 | 9128.9 | 9958.8 | 10788.7 | 11618.6 | 12448.5 | 13278.4 | 14108.3 | 14938.2 | 15768.1 | 16598 | 17427.9 | 18257.8 | 19087.7 | 19917.6 | 20747.5
Scada | 527 | 1054 | 1581 | 2108 | 2635 | 3162 | 3689 | 4216 | 4743 | 5270 | 5797 | 6324 | 6851 | 7378 | 7905 | 8432 | 8959 | 9486 | 10013 | 10540 | 11067 | 11594 | 12121 | 12648 | 13175
1510 Multi | 2704.99 | 3459.98 | 4214.97 | 4969.96 | 6699.95 | 7454.94 | 9184.93 | 9939.92 | 10694.91 | 11449.9 | 13179.89 | 13934.88 | 15664.87 | 16419.86 | 17174.85 | 17929.84 | 19659.83 | 20414.82 | 22144.81 | 22899.8 | 23654.79 | 24409.78 | 26139.77 | 26894.76 | 28624.75
1510 Line | 2138 | 2607 | 3076 | 3545 | 4014 | 4483 | 6621 | 7090 | 7559 | 8028 | 8497 | 8966 | 11104 | 11573 | 12042 | 12511 | 12980 | 13449 | 15587 | 16056 | 16525 | 16994 | 17463 | 17932 | 20070
Cost over X machines
Notes: Redo page less detail on makeup.

## Slide 12: Category Comparisons
Scada:
    Maintainability
      Less local experience
      Poor documentation
    Adaptability/software flexibility
      Two way MQTT communication, and ability to run SQL queries.
1510sp:
    All benefits of 1212C listed.
    Adaptability/software flexibility
      Can support more machines
      Supports Graph and STL programming
1212C:
    Maintainability
      Better local experience
      More industrialized
      Siemens documentation
    Adaptability/Software Flexibility
      IO Expansion allows more descriptive fail reporting
Chart: 
| Hardware Flexability | SoftwareFlexability | Initial Setup | Value
Scada Single Machine Solution | 2.8 | 10 | 10 | 6.8
1212C single Machine solution | 8.2 | 5 | 10 | 5
1510SP Multi Machine Solution | 9 | 5 | 5 | 3.6
1510SP Line Solution | 9 | 5 | 5 | 5.9
Weight | 7.34 | 7 | 3.7 | 1.6667
Better
Notes: Wrong slide not sure how it got in here fix
Organize better and displayin a ordered way based of weight.
Color the tops with which color they are and put in same order as bottom

## Slide 13: Hillsboro Recommendation
Siemens PLC 1510sp Line solution
    Environment
      Local experience
      Common development environment
      Easy troubleshooting
      Designed for an industrial setting
    Diverse Hardware
      More IO can allow for more complex error reporting
      Benefits of Scada IO can be added separately
    Flexible setup
      1 box is capable of up to 32 machines or 2 lines.
    Support
      More likely to get software/hardware support for longer (three year newer release date)
      Better support for MQTT
      Remote IO allows for a new CPU when this one loses support.
Pac Lite
Machine
Machine
Machine
HMI
HMI
Notes: Wrong slide not sure how it got in here fix

## Slide 14
Thank you.

## Slide 15: Backup Slides

## Slide 17
Chart: 

## Slide 18: Backup Slides
Chart: Cost Comparison
| Scada
CPU | 2580
Display | 444
Expansion IO | 0
Storage | 0
Misc | 192

## Slide 19: Cost Breakdown
 | HMI Cost | storage | Minimum Expansion
Siemens 1212 | $347 | $159 | $0
Siemens Using Remote IO 1510sp | $347 | $159 | $200
SCADA PIResistiveTouchscreen | $97 | $0 | $0
CPU | Cost Per Device | Cost Per New Machine | Cost per 4 | Straight Base | CPU cost | Accessory Cost
Siemens 1212C | $738 | $738 | $2,952 | $4,427 | $232 | $506
Siemens Using Remote IO 1510sp | $1,523 | $706 | $3,641 | $5,870 | $816 | $706
SCADA Resistive Touchscreen keyboard Mouse | $527 | $527 | $2,108 | $3,162 | $430 | $97
Cost For 4 Machines (best case for 1510)
Chart: 
| 1212C | 1510sp | SCADA
CPU | 926.6 | 816.46 | 1720
HMI | 1386.84 | 1386.84 | 388
Storage | 637.96 | 637.96 | 0
IO Expansion | 0 | 799.96 | 0

## Slide 20: Score Breakdown
 |  | Rating of Importance to Customer |  | 5.8 | 8.5 | 6.0 | 10.0 | 10.0 | 10.0 | 6.7 | 10.0 | 5.0 | 10.0 | 3.7 | 3.7 | 5.0 | 6.7 | 1.7 | 
 |  |  |  | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 
 |  |  |  | MQTT Support | Ability to heavy tasks without impacting realtime applications | Supports a Local HMI per machine | Experience of local engineers and E-Techs with the hardware/ software | Ease of remote administration | Repairability/ replacability | Commonly installed development environment | Software and Hardware documentation | Resident IO | IO Expandability | Complexity of initial setup | Adding restrictions from external software | support for multiple machines | report Complexity for part failure reasons | Cost | Total
Area of opportunity | Description of Improvement | Process Input |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Scada Single Machine Solution | Scada Box reporting to camstar with a local HMI Built in Node red and a remote administrative site in FreeBoard |  |  | 10 | 10 | 10 | 1 | 10 | 1 | 1 | 1 | 10 | 1 | 10 | 10 | 1 | 1 | 10 | 501.7
1212C single Machine solution | 1212C Siemens PLC Reporting a single machine to camstar with a local HMI |  |  | 5 | 5 | 10 | 10 | 5 | 10 | 10 | 10 | 10 | 10 | 10 | 5 | 1 | 10 | 5 | 833.3
1510SP Single Machine solution | 1510sp Siemens PLC Reporting a single machine to camstar with a local HMI |  |  | 5 | 5 | 10 | 10 | 5 | 10 | 10 | 10 | 10 | 10 | 10 | 5 | 1 | 10 | 1 | 826.7
1510SP Multi Machine Solution | a 1510SP CPU with remote IO, and HMI spread to each machine it is connected to. Limited to 4 machines |  |  | 5 | 5 | 10 | 10 | 5 | 10 | 10 | 10 | 10 | 10 | 5 | 5 | 5 | 10 | 5 | 835.0
1212C Multi Machine Solution | a 1212C with remote IO, and HMI spread to each machine it is connected to. Limited to 4 machines |  |  | 5 | 5 | 10 | 10 | 5 | 10 | 10 | 10 | 10 | 5 | 5 | 5 | 5 | 10 | 5 | 785.0
1510SP Line Solution | a 1510SP CPU with remote IO spread to each machine on a line. With 1 HMI at the end and beginning of the line only. Can support up to 32 machines. |  |  | 5 | 5 | 1 | 10 | 5 | 10 | 10 | 10 | 10 | 5 | 5 | 5 | 10 | 10 | 10 | 764.3
1212C Line Solution | a 1212Ccpu with remote IO spread to each machine on a line with 1 HMI at the end and beginning of the line only. Can support up to 32 machines. |  |  | 5 | 5 | 1 | 10 | 5 | 10 | 10 | 10 | 10 | 5 | 5 | 5 | 10 | 10 | 10 | 764.3