## Slide 1: Pac-Lite Service
Devlin Paddock | 06/28/2019
Light is OSRAM
Automotive

## Slide 2: Context
Changes in messaging
    Camstar no longer accepts MQTT.
    Germany is looking into a gRPC communication layer.
    Can only communicate with Camstar through TCP/IP or third party software.
    Can only talk to Engineering database through an API or SQL Commands.
Changes in Structure
    All Scrap is recorded in Engineering database not Camstar.
    Need for a more flexible communication layer.
Camstar
Pac Lite
Legacy Machines
Pac
Machines
MQTT Packets
MDE
Packetized data
UDP Packet
Digital IO
Old Model

## Slide 3: Pac Light Service
Service Interface
    Service for interfacing with many different Protocols.
    Easily change the communication methods for all Pac-Lite machines at one location
    One Universal interface for Pac-Lite to support.
    Documented Packet structure for importing information to Camstar, Engineering Database etc.
    Communicates to service through ActiveMQ in order to buffer data safely.
Pac-Lite
Pac-Lite
Pac-Lite
Pac-Lite
Pac-Lite
Pac-Lite
Pac-Lite
Pac-Lite
Pac-Lite Service
Camstar
ENG_DB
gRPC
TCP/IP
MQTT
gRPC Calls
ActiveMQ
SQL Queries
ActiveMQ

## Slide 4: Connection Choice
MQTT
    Publish, subscriber based connection good for abstraction.
    Small Packet sizes with reliable sending.
    Able to easily be sent from anything, whether it is a PLC/IPC or a Web/mobile application.
    Send and forget. Does not require any in depth maintenance for the connection. Good for low power or possibly unreliable networks.
    ActiveMQ Buffer Management.
Json
    Very simple name value pair.
    Much smaller and simpler than XML
    Able to easily be generated on anything from a PLC/ IPC to a Web or mobile application.
    Easy for low level programs to generate and high level programs to use in a class-full architecture.
    { “Machine": “Rat-Bat", “ResourceGroup":”XP1” , “Good":”42” , “Bad":”3”, “Index":”45” }

## Slide 5: Pac-Lite Packets
Packet Types
    Support created at the service level then implemented in PLC.
    Packet contains all information needed for further routing by the service
    Current Packet types are Throughput, Downtime, Index Summary.
    Max Packet Size of 260 Bytes, Max Payload of 246 bytes (~5% packet overhead)
Packet Header
Packet Type
Pac-Lite_ID
Reserved
JSON Pair/Values
1 Byte
1 Byte
1 Byte
5 Bytes
Up to 246 bytes
MQTT Header
6 Bytes

## Slide 6: Outputs Planned
ActiveMQ
    Consuming applications would subscribe to a topic and configure what type of packets they would receive.
    Naming Convention set per Topic.
Camstar
    TCP/IP connection to Camstar.
    Configure what packets it wants to receive and what packet format if applicable
SQL
    Specify which Database and Naming Convention.
    Auto Fills with data from packet.
gRPC
    Will be capable of calling gRPC procedures with packets setup and defined in the service.

## Slide 7: Thank you.
Automotive