## Slide 1: Intern Presentation
Devlin Paddock | 08/8/2019
Light is OSRAM
Automotive

## Slide 2: Introduction
Name:
Devlin Paddock
Location:
Concord, NH
School:
Graduate
Computer Engineering
NHTI, Concord, NH
Junior
Data Science / Computer Science
University of New Hampshire, Durham, NH

## Slide 3: The Project Interface Machines Without MDE to Camstar
Hardware Benchmarking
    Research and compare different hardware models and approaches.
    Benchmark these using Lean tools and methodology.
Service
    Connect Devices incapable of generating large complex packets to Camstar and other databases.
    Provide one interface to many databases for easier reporting from devices below the service
PLC Project
    Connect Legacy machines to the service developed.
    Avoids the cost of a PAC license and ongoing maintenance cost.
Camstar, SQL, Etc.
SNP Service
Legacy Machines
PAC
Machines
MDE
SNP
Raw Machine Signals
Packeted Data
Organized Calls

## Slide 4: SNP PLC Machine Data-Packager
Machine Interfacing
    Scrape signals directly off the machine with little to no existing machine/PLC modification.
    Very low development effort to rollout for additional lines.
    Allow product selection to support BOM enforced raw materials scanning and Camstar traceability.
Packetization
    Type chosen (MQTT,Json) due to very low overhead compared to other packet types.
    This type of packet is easy to generate on PLC.
    Allows for buffering and assured delivery through ActiveMQ.
Packet Header
Packet Type
Pac-Lite_ID
Reserved
JSON Pair/Values
1 Byte
1 Byte
1 Byte
5 Bytes
Up to 246 bytes
MQTT Header
6 Bytes
Packet Length
1 Byte
Null
1 Byte

## Slide 5: Results of the SNP project
Per Machine screen for control and more in depth information
Home Screen Displaying basic Information for each machine

## Slide 6: SNP Service Communication Interface
QRQC
Communication Protocol
    One communication interface to many data storage systems.
    Allows for very simple communication between complex devices.
Expandability
    Packet designed to accommodate many applications.
    Service built to handle thousands of packets a minute from multiple applications.
EMP
Other Producing App
OtherProducingApp
EMP
SNP
SNP
SNP
SNP
SNP Service
Camstar
gRPC
TCP/IP
MQTT
gRPC Calls
ActiveMQ Topics
SQL Queries
ActiveMQ
UDP
MDE/MDI
ENG_DB

## Slide 7: Results of the SNP project
Line automation
    Enable lines like XS, H7 or H11 to automatically report data to Camstar, and other databases.
    Make data available to new applications like QRQC and MDI.
    Provides BOM enforced raw material scanning.
    Opens up better reports for lines with limited data analytics.
API Access Point
    Allows for future applications (like SCADA BOX for environmental monitoring) to have an easy way to access many databases at once.
    Segregates all application packets allowing for internal payload to change drastically between applications to suit the applications needs.

## Slide 8: Expectations/Surprises
New Skills
    Learned many different data communication types and methods.
    Gained experience setting up and interfacing with an MQTT Broker.
    Expanded understanding of the .NET Framework and Siemens PLCs
    Collaborating with a global development team and benchmarking for a global solution.
Dealing With Real World Limitations
    Benchmarking hardware requires in-depth understanding of plant requirements.
    Natural scope creep. (Short Term Statistics and per index data collection)
    Large scale project redesigns. (Splitting application into PLC and Service)
    Interfacing with other applications being developed at the same time. (QRQC and MDI)
    Developing in a production environment with frequent priority shifts affecting resources.

## Slide 9: Future Impact On Studies and Personal Growth
    Develop systems with future changes in mind.
    It may be worth splitting a project in two to leverage benefits of two different technologies.
    Make clear and concise documentation.
    The real world is a lot messier than projects in school.

## Slide 10: Thank you.
Automotive

## Slide 11: Backup Slides.
Automotive

## Slide 12: Initial Requirements
Automotive

## Slide 13: Pac-Lite Project Requirements
Report Machine Output
    Up/Down status
    Good/Bad part output
    Machine indexes
    Empty head
    What product is being produced
    Enable power on
    10 Input to pac-lite
Display Machine Status
    Status stack light
    Easy to use HMI
    4 outputs from pac-lite
HMI
    Product selection- NAED
    Defined DT button
    Self managed NAED list
    Display diagnostics.
Sample UI on a Siemens HMI
New NAED
Enter
Sort
Camstar
Pac Lite
Legacy Machines
Pac
Machines
Scope of the project in orange
MDE
MQTT Packets
Digital IO
Cancel
Notes: Reduce slightly.

## Slide 14: Proposed Pac Light Architectures
One CPU per machine solution
    Provide a local HMI for user input, information and diagnostics display.
    Easy for E-Techs to troubleshoot
    Reliably record output of a single machine and report it to Camstar
One CPU per three machine solution
    Integration with up to three target machines
    Provide up to four remote HMIs for user input, information and diagnostics display.
    Reliably record output of up to three machines and report it to Camstar as separate machines.
One CPU per line solution
    One remote IO bundle per machine.
    Provides one display at beginning or end of line
    Reliably record output of up to 32 machines and report it to Camstar as separate machines.
Machine
Pac Lite
Pac Lite
HMI
HMI
HMI
HMI
Machine
Machine
Machine
Pac Lite
Machine
Machine
Machine
HMI
HMI
Notes: //Add original project def slide to backup slides. Add backup slides section after final slide.
//look into possibility of 1 HMI instead of 4. restriction was on HMI’s I believe that it was limited to 128 IO expansion at 8 per remote IO max.
//Check out support for communicating Between two plc’s in the 1200 series to allow switching the NAED at one location instead of two.
Replace diagrams on right with images of siemens pc’s
Shift slide 10-11 in as well

## Slide 15: Hardware Benchmarking
Automotive

## Slide 16: Score Breakdown
 |  | Rating of Importance to Customer |  | 5.8 | 8.5 | 6.0 | 10.0 | 10.0 | 10.0 | 6.7 | 10.0 | 5.0 | 10.0 | 3.7 | 3.7 | 5.0 | 6.7 | 1.7 | 
 |  |  |  | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 
 |  |  |  | MQTT Support | Ability to heavy tasks without impacting realtime applications | Supports a Local HMI per machine | Experience of local engineers and E-Techs with the hardware/ software | Ease of remote administration | Repairability/ replacability | Commonly installed development environment | Software and Hardware documentation | Resident IO | IO Expandability | Complexity of initial setup | Adding restrictions from external software | support for multiple machines | report Complexity for part failure reasons | Cost | Total
Area of opportunity | Description of Improvement | Process Input |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Scada Single Machine Solution | Scada Box reporting to camstar with a local HMI Built in Node red and a remote administrative site in FreeBoard |  |  | 10 | 10 | 10 | 1 | 10 | 1 | 1 | 1 | 10 | 1 | 10 | 10 | 1 | 1 | 10 | 501.7
1212C single Machine solution | 1212C Siemens PLC Reporting a single machine to camstar with a local HMI |  |  | 5 | 5 | 10 | 10 | 5 | 10 | 10 | 10 | 10 | 10 | 10 | 5 | 1 | 10 | 5 | 833.3
1510SP Single Machine solution | 1510sp Siemens PLC Reporting a single machine to camstar with a local HMI |  |  | 5 | 5 | 10 | 10 | 5 | 10 | 10 | 10 | 10 | 10 | 10 | 5 | 1 | 10 | 1 | 826.7
1510SP Multi Machine Solution | a 1510SP CPU with remote IO, and HMI spread to each machine it is connected to. Limited to 4 machines |  |  | 5 | 5 | 10 | 10 | 5 | 10 | 10 | 10 | 10 | 10 | 5 | 5 | 5 | 10 | 5 | 835.0
1212C Multi Machine Solution | a 1212C with remote IO, and HMI spread to each machine it is connected to. Limited to 4 machines |  |  | 5 | 5 | 10 | 10 | 5 | 10 | 10 | 10 | 10 | 5 | 5 | 5 | 5 | 10 | 5 | 785.0
1510SP Line Solution | a 1510SP CPU with remote IO spread to each machine on a line. With 1 HMI at the end and beginning of the line only. Can support up to 32 machines. |  |  | 5 | 5 | 1 | 10 | 5 | 10 | 10 | 10 | 10 | 5 | 5 | 5 | 10 | 10 | 10 | 764.3
1212C Line Solution | a 1212Ccpu with remote IO spread to each machine on a line with 1 HMI at the end and beginning of the line only. Can support up to 32 machines. |  |  | 5 | 5 | 1 | 10 | 5 | 10 | 10 | 10 | 10 | 5 | 5 | 5 | 10 | 10 | 10 | 764.3

## Slide 17: Score Breakdown

## Slide 18: Hillsboro Recommendation
Siemens PLC 1510sp Line solution
    Environment
      Local experience
      Common development environment
      Easy troubleshooting
      Designed for an industrial setting
    Diverse Hardware
      More IO can allow for more complex error reporting
      Benefits of Scada IO can be added separately
    Flexible setup
      1 box is capable of up to 32 machines or 2 lines.
    Support
      More likely to get software/hardware support for longer (three year newer release date)
      Better support for MQTT
      Remote IO allows for a new CPU when this one loses support.
Pac Lite
Machine
Machine
Machine
HMI
HMI
Notes: Wrong slide not sure how it got in here fix

## Slide 19: Camstar Packet Sending
Automotive

## Slide 20: Scada Box
Packet Setup
    __session always connecting by sending username and password in the attached XML Sample and encoding with the Camstar Dll’s
    Any number of services. Can come before the execute tag. Currently I’m using ResourceThruput and ResourceSetupTransition
    <__execute/> needs to be present to execute the service. Otherwise it just queries the information.
    You must request a completion message in request data otherwise you will receive no indication of weather it succeeded or failed.
    Make sure you use the Correct XML Header. Check a tracked packet to see which xml version and encoding version you should be sending.

## Slide 21: Scada Box
Sending Setup
    Currently I am just sending it through a TCP Connection to Camstar.
    Camstar will accept any TCP connection request on the correct Ip and port and gracefully disconnect without warning.
    Just send the data to that port then read the return message if requested
    You must request a completion message in request data otherwise you will receive no indication of weather it succeeded or failed.

## Slide 22: Scope Creep/Database questions
Automotive

## Slide 23
Automotive

## Slide 24: Miscellaneous other projects
Automotive

## Slide 25
Automotive
Machine Manager for creating all resources needed for a new line (except Camstar resources) on SNP
MQTT Batch sender
TestMessage Generator
TestLine Service
Service Installer Application

## Slide 26: More info on this project can be found at https://lightweb.osram-light.com/content/10003873/HIEDO/IND40/CAMSTAR/ under documents/presentations/ intern presentations/ Devlin/ SNPDocumentation
Automotive

## Slide 27: External Hobbies
Automotive

## Slide 28
Automotive